## Slide 1: Sensors
FeMaidens Programming 2017-2018
Lily and Marisa

## Slide 2: What are sensors?
Sensors are devices that measure, output and sometimes respond to information about the position (or other characteristics) of the robot that we can use when driving or using the robot!
Many different sensors output different types of useful information
Some examples of sensors that we use are:
  Encoders
  Gyro
  Ultrasonic
  Camera

## Slide 3: Encoders
Main purpose: To measure the distance that the robot has driven based on how much the wheels have moved
How they work: Encoders measure distance in terms of ticks, which are converted into usable information like this
  While the robot is moving, the encoder gives us the number of ticks that it has measured
  Each revolution (full turn) of a wheel is equal to a certain number of ticks
  By dividing the number of ticks (that the encoder recorded), by the ticksPerRev, you get the number of turns that the wheel has made
  Then, multiply the # of turns made by the wheel * the circumference (in usable units), to get the total distance travelled

## Slide 4: Encoders (Cont.)
Ticks turned
Ticks in one revolution
X
Circumference of wheel

## Slide 5: Gyro
Main purpose: To measure the degrees that the robot has turned over a certain period of time, which can help us align the robot
How they work:
  Important Functions:
    getRate() - returns the rate of rotation
    getAngle() - returns the angle that the robot is currently facing
    reset() - resets the gyro value to 0 → used to recalibrate, used in initialize
  To make the robot drive straight, we compared the angle that the robot was facing to the angle that the robot is currently facing, and then set the left or right motors accordingly

## Slide 6: Ultrasonic Sensors
Main purpose: To measure the distance to object and any obstruction (like echo-location that whales/bats use)
How they work:
  A high-frequency sound wave is sent out from the sensor
  The sound wave will continue moving forward until it hits something
  The sound wave will bounce back from the object it hit. It will then reenter the sensor
  The sensor then calculates the distance between the sensor and the obstruction

## Slide 7: Ultrasonic (con’t)

## Slide 8: Camera
Main purpose: When attached to the robot, it can be used to have a better view of field objects (video is “live- streamed” on computer). This helps us target specific objects.
Notes: Talk about retroreflective tape

## Slide 9: Camera (Cont.)
How they work:
  A library called OpenCV is used to isolate/get info from the desired objects (ex: retroreflective tape)
    A light is directed towards the retroreflective tape (green light usually)
    The tape becomes illuminated with the color of the light directed at it
    The image from the camera is blurred
    The specific shape and color the tape is used to target the desired object